## Slide 1: Wi-Fi™ Module Product Training
April, 2012

## Slide 2: Wi-Fi™ Overview
Protocol
  Built on the IEEE 802.11 standard
  Conformance testing performed by the non-profit Wi-Fi Alliance (formed in 1999)
Consumer Wi-Fi Growth (2009 - 2010)
  158% growth in Wi-Fi enabled consumer electronics
  90% cell phones
  3 in 4 consumers considered buying a Wi-Fi enabled device
    34% laptops
    15% Wi-Fi connected 3-D TVs
Embedded Systems
  Evangelizes on huge hotspot availability
  Provides data with ultra-low cost transport

## Slide 3: Wi-Fi™ Overview
Roving Networks’ Wi-Fi Solution
  Industry’s lowest power, complete system-on-module solution
    4-uA sleep
    30-mA Rx
    Tx variable depending on PA options
  Compact surface mount design
  Quick & simple to integrate
  Complete TCP/IP solution: no external processor or drivers required
Feature Rich, Robust Firmware
  Standard build: serial port profile
  Extensions: WebScan™ & sensor

## Slide 4: Firmware
April, 2012

## Slide 5: Roving Networks Firmware
Standard Firmware
  Simplifies customer design
  No register-level configurations
  Manages standard TCP/IP service, e.g., HTTP, DHCP, FTP
Firmware Extensions
  Builds on the robust, standard firmware
  Provides application-specific extensions
    Sensor
      Remote provisioning
      Automatic sensor data acquisitions
      Data logging
    WebScan™
      RTLS (Real-Time Location System)

## Slide 6: Firmware Extensions
Sensor: Real-Time Monitoring
  Uses Roving Networks silicon
  Monitors I/O pin & ADC status
  Data logger
    If module disconnects from access point, it stores data until reconnect when data can be sent to server
  Supports remote provisioning
  Supports remote software upgrade

## Slide 7: Firmware Extensions
WebScan: Real-Time Location System
  Uses Roving Networks silicon
  Uses I/O pins, ADCs, RFID & timers for wakeup & data generation
  Measures RSSI levels for triangulation
  Creates full data packet for server upload

## Slide 8: Firmware Extensions
WebScan Example Application
Goods monitored by tag attached to pallet
Pallets arrive at docking bay A
Tag wakes by MAG exciter near docking bay door
Tag probes for access points & measures their RSSI level
Tag sends RSSI data to company’s server via Wi-Fi
Tag reports logged data
  Refrigeration truck temperatures
  Tag wake up reasons
  Battery life

## Slide 9: Wi-Fi Lab: Introduction
April, 2012

## Slide 10: Lab Agenda
Introducing WiFly
  Firmware
  Hardware architecture
  Capabilities
Hands-On Wi-Fi Labs
  Association & UDP
  TCP connections & embedded applications
  Roaming & FTP
  HTML client & sensors
  Location tracking (optional)
  Ad hoc & further FTP (optional)
Resources

## Slide 11: Data & Command Modes
Data Mode (Default State)
  WiFly module like data pipe
  TCP/UDP header stripped or added, transparent to UART
  Data written to UART is sent out over Wi-Fi
  Data received over Wi-Fi is read from UART
Command Mode ($$$)
  Special configuration mode entered using $$$
  Used to assign data, e.g., SSID, pass phrase, etc.
A
B

## Slide 12: Command Mode: Configuration Settings
Performed Using ASCII Commands
  User Guide
Configuration Settings Stored in Module’s Flash
  Changes are persistent & reloaded after power cycling
  Changes kept using save command
  Many settings require reboot to take effect

## Slide 13: Command Mode: Syntax
Commands Use Keyword Followed by Additional Information
Command Rules
  Case sensitive
  Spaces not allowed, substitute $ “MY NETWORK” = “MY$NETWORK”
Can Use Shorthand
  set uart baudrate 115200 valid
  set uart b 115200 valid
  set u b 115200 valid
  s uart baudrate 115200 Invalid

## Slide 14: Command Mode: Keywords
Set: Immediate Effect, Permanent If Saved to Configuration File
Get: Retrieve & Display Permanently Stored Information
Status: Current Interface Status, IP Address, etc.
Action: Perform Actions Such As Scan, Connect & Disconnect
File: Upgrade, Load & Save Configuration, Delete Files, etc.
Set Command | Function
AdHoc | Controls the ad hoc parameters
Broadcast | Controls the broadcast hello/heartbeat UDP message
COMM | Communication & data transfer, matching characters
DNS | DNS host & domain
FTP | FTP host address & login information
IP | IP settings
Option | Optional & infrequently used parameters
Sys | System settings such as sleep & wake timers
Time | Real-time clock settings
UART | Serial port settings such as baud rate & parity
WLAN | Wireless interface, such as SSID, channel & security options

## Slide 15: Hardware Architecture: Key Features
2.4-GHz IEEE 802.11b/g Tx/Rx
Ultra Low-Power Consumption
  4-uA sleep
  40-mA RX/connected
  200-mA maximum TX
Sparc 32-Bit Micro
  Embedded TCP/UDP/IP stacks
Hardware Interfaces
  UART: 1-Mbps streaming
  SPI slave: 2.7-Mbps streaming
10 GPIO Pins
  Status & control
8 Analog Sensor Inputs
  14-bit, 35-us frequency
  0 to 1.2 V
Security: Hardware Encryption Engine
  WEP128
  WPA-PSK
  WPA2-PSK (TKIP & AES)
Real-Time Clock
1-MB Flash Memory for Data Logging
2-KB NV RAM
Battery Boost Regulator

## Slide 16: Hardware Architecture: Silicon

## Slide 17: Hardware Architecture: Development Environment

## Slide 18: Wi-Fi Lab
April, 2012

## Slide 19: Lab Prerequisites
Hardware
  RN-134-K or RN-174-K evaluation kit
  Configured access point (AP)
    Security: WEP-128, WPA-TKIP or WPA2-AES
  FTP server to upload & store data
Utility Software
  Available from http://www.rovingnetworks.com support page
  Tera Term (terminal emulator)
  PortPeeker (packet sniffer)

## Slide 20: Lab 1: Association & UDP
Lab Overview
  Infrastructure & ad hoc networks
  Hardware setup
  Configuration parameters & factory resets
  Scan, join & authenticate
  Broadcast UDP
  Device name
  Sensor mask
  UDP auto-pair

## Slide 21: Lab 1: Association & UDP
Supported Security Modes
  WEP 64, WEP 128 OLD/NOT SECURE
  WPA1 TKIP
  WPA2 AES has not been compromised
  Enterprise not currently supported
Finding Devices on Network
Roving Networks Device
192.168.0.3
Access Point
DHCP server
Roving Networks Device
192.168.0.2
192.168.0.1
174.201.25.16
To Internet
Infrastructure Networking
Roving Networks Device
Roving Networks Device
Roving Networks Device
Roving Networks Device
169.254.1.1
169.254.1.2
169.254.1.3
169.254.1.3
Ad Hoc Networking

## Slide 22: Lab 1: Hardware Setup
Connect Evaluation Board
  Connect board to your computer
  Connect battery
    Blue LED lights up (RN-134-K only)
    Green LED blinks slowly
  Use device manager to find the COM port

## Slide 23: Lab 1: Configure Module via UART
Launch Command Mode
  Run Tera Term
  Open assigned COM port
    Serial port settings: 9600 baud, 8 bits, No Parity, 1 stop bit
  Type $$$
  Module responds with <CMD>
Review & Reset Configuration
  Check configuration & firmware version
    get e
    ver
  Perform factory reset (starts module in known state)
    factory R
    reboot
Notes: Write down module’s IP address.

## Slide 24: Lab 1: Joining/Associating with Networks
Search for Networks
  $$$ (enter command mode)
  scan
Join a network
  join # 1 (remember spaces)
  leave
  join <string> (e.g., join RovingNET)
  leave
Auto-Join Network with Persistent Configuration
  set wlan ssid <string>
  set wlan pass <string>
  save
  reboot
TIP: If Network Is Secure, Set Pass Phrase with set wlan pass <string> before Joining Network

## Slide 25: Lab 1: Interim Summary
Configured Module via the UART in Command Mode
Next, Observe Wi-Fi Activity Using PortPeeker

## Slide 26: Lab 1: Configure & Capture UDP with PortPeeker
Associate PC with Same AP as Module
  Enter command mode & retrieve module’s IP address
  Ensure PC is on same subnet
Launch & Configure PortPeeker
  Click configure
  Set port number to 55555 (default)
  Set protocol to UDP
  Click OK
Start UDP Packet Capture
  Click Start
  If PC & module are on same subnet, broadcast packets shown
  If multiple nodes on network, look for YOUR IP address

## Slide 27: Lab 1: UDP Broadcast
Module Sends UDP Broadcast at Specified Intervals
UDP Broadcast Contains Information that Identifies Module on Network
Set UDP Broadcast Interval
  Enter command mode
    get broadcast (observe current interval)
    set b i 3 (b=broadcast, i=interval)
    save & reboot
  Review UDP messages in PortPeeker
Enable Sensor Data in UDP Broadcast
  Enter command mode
    set q s 0xff (set sensor mask)
    save to make persistent
  Reboot not required
  Review UDP messages in PortPeeker
    Sensor data highlighted
Notes: After typing ‘get broadcast’ observe interval in Tera Term
Set b I 3

## Slide 28: Lab 1: Setting Device Name
Device Names Can Identify Products on Network
Can Append Device ID to UDP Broadcast
Set Device ID
  Enter command mode
    get option
    set o d RockAndRollWiFi (o=optional, d=deviceID)
    save & reboot
  Review UDP messages in PortPeeker
Set Broadcast UDP Port
  Enter command mode
    get broadcast
    set b p 50000 (b=broadcast, p=port)
    Save & reboot not required
  Reconfigure PortPeeker to listen for UDP packets on port 50000
  Review UDP messages in PortPeeker
TIP: UDP Broadcast on by Default Set Interval to 0 to Turn It Off
Notes: JoinTmr = time will to wait for AP (WiFi std is 250mS, we set default to 1000mS since DLink is slow)
Replace = 0x24 - this si the alternative character ($)
Remember if someone uses a space then they need to remember to use a replacement character else the latter part of the name will be missing.
See current port number with get broadcast, should be 55555 from earlier. Set b p 50000 will change it. Note PortPeeker will stop seeing the broadcast.
What will happen if you changed the BCAST from 255.255.255.255 to a specific address? – Message is sent to that particular address, not entire subnet.

## Slide 29: Lab 1: Sending UDP Packets
UDP Mode Not Enabled by Default
Enable UDP by Setting Remote Host, Port & Protocol
  Enter command mode
    factory R
    Associate with AP
    set ip host <address>
    set ip remote 50000
    set ip proto 1 (IP protocol bitmask; 1 = UDP)
    set comm timer 1000 (try 10, see the change)
    get ip
    save & reboot
  Type characters; they appear in PortPeeker
TIP: IP Protocol Value Is a Bit Mask You Can Enable Both TCP & UDP Messages

## Slide 30: Lab 1: UDP Auto Pairing Mode (Optional Slide)
Similar to Bluetooth Pairing, Module Can Store IP Addresses for Fast UDP Message Setup
Example Requires 2 Modules
Module 1: Clear Host IP & Port & Set Auto Pair Mode
  $$$ (enter command mode)
  set ip host 0.0.0.0
  set ip remote 2000
  set ip local 2000
  set ip flag 0x40
  save & reboot
Module 2: Set Module 1 Host IP & Port
  $$$ (enter command mode)
  set ip host <module 1 address>
  set ip remote 2000
  set comm timer 1000
  save & reboot
Test System
  Type characters in module 2’s terminal; they appear in module 1’s terminal window
  Type characters in module 1’s terminal; they appear in module 2’s terminal window
Notes: Setting ip host to 0.0.0.0 ensure unit doesn’t talk to anyone
The magic comes about because module 1 learns the address when module 2 talks to it.

## Slide 31: Lab 1: Conclusion
RN-134-K or RN-174-K with Terminal Emulator & Serial Cable Provides Simple, Effective Development Environment
Joining Networks Is Easy
Use Broadcast UDP to Find Modules on Network Using Device Names & MAC Addresses
Module Sends UART Data as UDP Packets when Associated with Network in UDP Mode

## Slide 32: Lab 2: TCP
Objective
  Connect from module to remote host using TCP
  Connect to module from remote host using TCP
  TCP modes
  Auto-connect features
  Alternative GPIO functions
  Event-based TCP packet forwarding
Prerequisites
  RN-134-K set up as in Lab 1
  Module associated to access point (AP)
  Computer associated to same AP
  Telnet client (Tera Term)
  PortPeeker application

## Slide 33: Lab 2: TCP Connections
WiFly Module Opens TCP Connection
Sensing applications
Sending data to web server
Data acquisition systems
Fleet management
RN-134-K
192.168.1.50
Listen on Port 2000
Access Point
DHCP server
Remote Host
192.168.1.200
Listen on Port 5000
Remote Host Opens TCP Connection
Industrial controls
Home automation
Universal remotes
open 192.168.1.200 5000
open 192.168.1.50 2000
TCP Connections Are Point to Point
Provide Reliable, Guaranteed, In Order Data Delivery
Also Known As Sockets

## Slide 34: Lab 2: Setup PortPeeker
Associate Computer with AP
Launch PortPeeker
Configure PortPeeker
  Click Configure (Note PC’s IP address in Interface box)
  Set port to 5000 (port number matches remote port of WiFly module)
  Set protocol to TCP
Click Start to Capture TCP Packets

## Slide 35: Lab 2: Open TCP Connection from Module
With Module Connected to PC over USB-Serial Cable, Open Tera Term on Serial COM Port
Restore Module to Factory Defaults
  Enter command mode
  factory R
  Associate with AP
  save & reboot
Open TCP connection
  open <remote host address> 5000
  *OPEN* shown on serial port (Tera Term window) & packet with *HELLO* on PortPeeker
Close TCP Connection
  Enter command mode
  close
  Close string *CLOS* displayed in Tera Term

## Slide 36: Lab 2: Connecting from Remote Host to WiFly module
In Command Mode, Obtain Module’s IP Address
  get ip
Open Telnet Connection from PC Using Tera Term (Use Existing Instance)
  Click File > New connection
  Select TCP/IP
  Select Telnet
  In Host field, type module’s IP address
  TCP port# is 2000 (default listening port)
  Click OK
*HELLO* Message Shown in Telnet Window Indicating Successful TCP Connection
Type in Telnet Window; Data Appears on Serial Port Window & Vice Versa
Can Configure Module Remotely over Telnet by Entering Command Mode
*HELLO*
Notes: Don’t open a new Tera Term – open a new connection within the existing instance.

## Slide 37: Lab 2: TCP modes
Module Supports Three TCP Modes
  TCP client & server mode
    Default mode initiates & accepts TCP connections
    Currently supports one active connection at a time
    Concurrent TCP connections supported in future
  TCP client ONLY mode
    ONLY initiates TCP connections; cannot accept incoming connections
  Secure mode
    ONLY receives packets from host that matches stored host IP address
  TIP: Refer to User Manual for More Details on TCP Modes

## Slide 38: Lab 2: TCP Client Mode
Set Up Module in TCP Client Mode
  set ip proto 8
  save & reboot
Open New Telnet Connection to Module from Tera Term
Second Connection Is Refused Indicating TCP_Client Mode Works Correctly

## Slide 39: Lab 2: Auto-Connect Feature
Module Can Automatically Open TCP Connection to Remote Host on Power Up or Waking from Sleep
Auto-Connect Controlled by autoconn Setting
  set sys auto 1 // Attempts to open TCP connection immediately once only
  set sys auto <value> // Attempts to open TCP connection every <value> seconds
  set sys auto 255 // Attempts to open TCP connection once & go back to sleep immediately // when connection is closed
Auto-Connect Requires Module to Store Remote Host’s IP Address & Port #
  set ip host <host IP address>
  set ip remote <port>
Once TCP Connection Is Opened, It Can Be Closed in Several Ways
  close command
  Idle timer
  Remote host
Idle Timer Closes TCP Connection after Preset # of Seconds of No Activity (No Tx or Rx) on the TCP Link
  set com idle <value> //Closes the TCP connection after <value> seconds of inactivity
Notes: Nothing will be typed into the module on this slide. This is just an intro.

## Slide 40: Lab 2: Auto Connect Feature (Timers)
Module Attempts a TCP Connection Every 10 seconds, Drops Connection after 3 seconds Inactivity
  set ip host <address>
  set ip remote 5000
  set sys auto 10
  set comm idle 3
  save
  reboot
PortPeeker: Connection Opens & Closes
Tera Term: Open & Close Strings Shown when Each Connection Opens & Closes
*OPEN**CLOS*…

## Slide 41: Lab 2: Alternative GPIO Functions
Firmware Uses GPIO 4, 5 & 6 to Blink Evaluation Board’s Status LEDs (See Section 2.4 in User Manual for Standard LED Function)
Microcontroller Opens or Closes TCP Connection to Stored Remote Host by Driving GPIO5 High or Low
  This setup requires a hardware configuration that is not part of this lab
Microcontroller Can Monitor TCP Connection Status by Reading GPIO6
  High = Connected
  Low = Not Connected
GPIO | Function | Description
4 (GRN) | Output | High once associated, authenticated & has IP address.
5 (RED) | Input | Set high to trigger TCP connection, low to disconnect.
6 (YLW) | Output | High when connected over TCP, low when disconnected.

## Slide 42: Lab 2: Alternative GPIO Functions
Enable Alternative Functions
  set wlan ssid <string>
  set sys iofunc 0x70
  save
  reboot
  Evaluation board LEDs do not turn on
After Module Associates with AP
  Associate with AP
  save & reboot
  Green LED goes on (GPIO4)
Connect/Disconnect TCP Connection
  Enter command mode ($$$)
  open <address><value>
  Red LED blinks & connection closed because RN-134-K board’s GPIO5 pulled to GND
  Enter command mode ($$$)
  leave // disassociate from AP
  Green LED goes OFF

## Slide 43: Lab 2: Setting Comm Strings
Microcontroller Can Look for UART comm Strings as Indication of TCP Connection Status
  Factory reset
  reboot
  Associate with AP
  set ip host <address>
  set ip remote 5000
  set comm open HAPPY
  set comm close HOLIDAYS
  set comm remote HAPPY_NEW_YEAR
  save & reboot
  Enter command mode
  open
  See open string in Tera Term
  See remote string in PortPeeker
  Enter command mode
  close
  See close string in Tera Term
Tip: Microcontroller Can Read UART Open & Close Strings to Determine TCP Connection Status

## Slide 44: Lab 2: Forwarding TCP packets
When Data Is Written to Module’s UART, TCP Packets Forwarded Based On
  Flush timer
  Flush size
  Match character
TCP Packet Sent When Any of These Events Occur
Parameters Logically ORed to Determine when TCP Packet Is Sent
When Configured Correctly, Module Can Be Optimized for Low Latency or High Throughput
  Low latency: use lower flush timer value & flush size
  High throughput: use higher flush timer value & flush size
Tip: Module Tries to Optimize Automatically for Bandwidth by Increasing Default Flush Size with Higher Baud Rates

## Slide 45: Lab 2: Forwarding TCP packets
Forwarding Packets Based on Flush Timer
  set comm timer 1000
  save
  open
  Type text after TCP connection opens
  After you stop typing, TCP packet is sent 1 second later
Forward Packets Based on Match Character
  set c t 0 (why do we send this command ?)
  set comm match 65
    This parameter expects ASCII decimal character or HEX value of the match character (e.g., 65= Capital A)
  save
  open
  Type 12345678A
  TCP packet sent out after you type A character
  Observe packet in PortPeeker
What Do You Learn from Using ‘get c’ Command?

## Slide 46: Lab 2: Conclusion
Module Can Open TCP Connection to Remote Host & Accept Incoming Connections from Remote Host
Auto-Connect Automatically Opens TCP Connection
Idle Timer Can Automatically Close TCP Connection
Alternative GPIO Functions Allow Microcontroller to Control & Monitor TCP Connections
comm open, close & remote Strings Can Indicate TCP Connection Status
TCP Packets Forwarded Based On
  Packet size
  Match character
  Flush timer

## Slide 47: Lab 3: Association/Roaming & FTP
Objective
  Wake & sleep timers
  Auto join
  Roaming configuration (Linkmon/IP flags)
  FTP
Prerequisites
  User has completed Labs 1 & 2
  Evaluation board & computer set up as described in Lab 1

## Slide 48: Lab 3: Where in the World Wide Web are you?
Module Associates with AP Based on SSID
  Password required depending on security
  Multiple security modes
  Multiple AP with same SSID and/or password
Each Wi-Fi Device Must Have Unique IP Address
  Provided by DHCP server
  Gateway bridges multiple networks, typically Internet with Intranet
  Dynamic Name Service (DNS)
    Maps URL (www.google.com) to an IP Address 74.125.19.103
Access Point
SSID RovingNet1
Bridge
Roving Networks Device
To internet
Intranet
Local Network
Access Point
SSID RovingNet
DHCP server
192.168.0.1
Roving Networks Device
192.168.0.2
101.11.2.15
Router
DHCP server
Gateway
10.10.10.1
Internet
Worldwide Web
10.10.10.2
10.10.10.3
10.10.10.3
10.10.10.4
DNS server
www.google.com
135.201.25.15
74.125.19.103

## Slide 49: Lab 3: Wake & Sleep Timers
Several Options to Wake Module
  FORCE WAKE Signal
  Sensors
  Internal Timers
Restore Factory Default Parameters & Training AP
  Enter command mode
  factory R
  Associate module with AP
  save & reboot
Set Wake Timer: # Seconds in Deep Sleep before Wake Up
  set sys wake 10
Set Sleep Timer: # Seconds before Entering Deep Sleep
  set sys sleep 5
  save & reboot
  LEDs cycle on & off (except blue),
  Observe module reboot on wake up in Tera Term
TIP: Do Not Set Sleep Timer to Less than 2 Seconds or It Is Hard to Go into Command Mode & Reconfigure Module before It Sleeps Again

## Slide 50: Lab 3: Join Modes
Useful for Module to Associate with Network Automatically
Association Controlled with join Command or join Parameter Setting
Turn Off Auto-Join & Join Manually
  Enter command mode
  factory R & reboot
  Associate module with AP
  set wlan join 0
  save & reboot
  Enter command mode
  Join
  Modules associates with AP
Auto-Associate with Any Open-Security AP
  set wlan ssid <string>
  set wlan join 2
  set wlan auth 0
  save & reboot
  Module attempts to join any open network (no security)
TIP: If Network is Secure, Set Pass Phrase with “set wlan pass <password>” before Joining Network
Value | Policy
0 | Manual. Do not join automatically.
1 | Attempt to join the AP that matches the stored SSID, pass phrase & channel. Channel can be set to 0 for scanning. (Default)
2 | Join any AP with security matching the stored authentication mode. This setting ignores the stored SSID and searches for the AP with the strongest signal. The channels searched can be limited by setting the channel mas.
3 | Reserved. Do not use.
4 | Create an ad hoc network using the stored SSID, IP address & netmask. You must set the channel.

## Slide 51: Lab 3: Roaming (Optional Slide)
Module Wakes, Searches for Aps, Connects, Off Loads Data & Returns to Sleep
Used for Asset Tracking, Fleet Management & Remote Sensor Applications
Combine Broadcast UDP, Wake Timers & Auto Join
  Enter command mode
  factory R & reboot
  set broad interval 3
  set opt device <string>
  set wlan join 2
  set wlan auth 0
  set sys sleep 15
  set sys wake 5
  save & reboot
Open PortPeeker to Receive UDP Broadcast Messages (Lab 1)
Confirm Module’s UDP Broadcast Message
Move Module Near AP_SSID1 AP
Move Module Near AP_SSID2 AP
  PortPeeker shows AP MAC address in broadcast UDP message change

## Slide 52: Lab 3: FTP Update (REQUIRES Internet Access)
Use Module’s FTP Client to Update Firmware & Put/Get Data
Default Username/Password Set to Roving Networks’ FTP Server
Associate to Internet-Connected Network & Use “ftp update” Command
Use Local FTP Server
  Enter command mode
  factory R
  Associate module with AP
  save & reboot
Update Firmware
  Enter command mode
  ftp update
  ver
  reboot
  Enter command mode
  Ver
TIP: After Downloading New Firmware, Restore Module to Factory Defaults Before Using It

## Slide 53: Lab 3: Setting Firmware Boot Image
Firmware Stored in Embedded Flash Memory
Boot Image is Firmware Version Module Is Currently Running
After Successful Update, Boot Image Changes to New Firmware File
Change Boot Image
  Enter command mode
View Files in Flash
  Enter command mode
  ls
Change Boot Image
  Enter command mode
  boot image <value>
  reboot

## Slide 54: Lab 3: FTP put & get
FTP Client Can Stream Files to/from FTP Server
  Useful in data logger applications
FTP Servers Can Accept Multiple Clients Concurrently
Configure FTP Setup
  Enter command mode
  factory R & reboot
  Associate module with AP
  set ftp address <address> (e.g., ftp svr addr)
  set ftp user <string> (e.g., roving)
  set ftp pass <string> (e.g., Pass123)
  set ftp dir <string> (e.g., public)
  set ftp timer 20
  save & reboot
Create & Read File on Server
  Enter command mode
  ftp put <string>
  Type characters, wait until *CLOS* shown
  ftp get <string>

## Slide 55: Lab 3: Conclusion
Sleep & Wake Timers Allow Module to Deep Sleep to Save Power & Periodically Connect to Network
Roaming Allows Module to Connect to AP with Strongest Signal that Matches SSID or Authentication Mode
Use FTP to Update Firmware
Use FTP put & get Commands to Transfer Files
FTP put Combined with Sleep/Wake/Roaming Useful for Data Logging Applications

## Slide 56: Lab 4: HTTP Client
Objective
  Post data to web server
    Uses built-in feature
    Does not require external processor
  Configure HTTP client mode
  Periodically send sensor data web server
  Wake on UART data
Prerequisites
  Hardware same as in previous labs
  Module associated to Access Point (AP) with Internet connectivity
  Tera Term running on PC
  Web server configured to accept HTTP messages (Roving Networks Website)

## Slide 57: Lab 4: Solutions Architecture

## Slide 58: Lab 4: Enabling HTTP Client Mode
HTTP Client Mode Disabled by Default
  To enable use set ip proto 18 command
Module Connects to Web Server Using the IP Address or URL
Web Server Listens on Port 80 (Default) for Incoming Connections
For Each Request
  Web server responds with 200 OK
  Closes the connection

## Slide 59: Lab 4: Auto-Posting Sensor Data
In HTTP Client Mode, Module Sends Request Message
  GET /server.php?value=0F3000001111222233334444555566667777\n\n
  Request message includes comm remote string & sensor readings
Configure HTTP Client Mode & Request Message
  Go into command mode
  Associate the module with AP
  set ip proto 18 // Enable HTTP & TCP protocols
  set ip host 0 // Set IP address if known
  set dns name www.rovingnetworks.com // Set DNS name if not
  set ip remote 80 // Standard web server port
  set comm remote GET$/server3.php?value= // $ is replaced by space character
  set q sensor 0xff // Sample all sensors inputs
  set option format 7 // Send header & sample sensor data
  save & reboot
  Enter command mode
  open
Format
2 Bytes GPIO | Chan 0 | Chan 1 | Chan 2 | Chan 3 | Chan 4 | Chan 5 | Chan 6 | Chan 7
0F30 | 0000 | 1111 | 2222 | 3333 | 4444 | 5555 | 6666 | 7777

## Slide 60: Lab 4: Web Server
*OPEN*HTTP/1.1 200 OK
Date: Fri, 19 Nov 2010 19:24:07 GMT
Server: Apache
X-Powered-By: PHP/5.2.13
Connection: close
Content-Type: text/html
Server accepted values <br />
ID: 0<br />
VALUE: 0D16CF2907ED3EB640AB07E607F4321C3219
RTC: 0
*CLOS* GPIO values Sensor Data
Open Web Browser
  The PC must be associated with your AP connected to the internet
In Address Bar, Type www.rovingnetworks.com/result.htm
  Scroll to bottom of log to see data
  All module data looks the same

## Slide 61: Lab 4: Add Device Name & RTC to Sensor Data
Append Device ID & RTC Value to Sensor Data so Server Can Identify It
  Device String: Appends &id=<value>, where <value> is device ID string set with set opt device <string> command
  Real-Time Clock: Appends &rtc=<time>, where <time> is real-time clock value in message as 32-bit HEX value in format aabbccddeeff
Turn Off Auto Connect
  Go into command mode
  Set sys auto 0
  Save & reboot
Append Device Name & RTC
  Go into command mode
  set option device <string>
  time // Get network time
  set option format 31
  save & reboot
Post Data
  Go into command mode
  open
Tera Term Output
*OPEN*SEND-WEBPOST
HTTP/1.1 200 OK
Date: Mon, 06 Dec 2010 17:56:28 GMT
Server: Apache
X-Powered-By: PHP/5.2.13
Connection: close
Content-Type: text/html
Server accepted values <br /> Device ID
ID: servertest<br />
VALUE: 0D16CF2908043E854020080108043236323A
RTC: 3ad82
*CLOS* Real Time Clock

## Slide 62: Lab 4: Auto-Posting UART Data
Module Can Wake on Receiving UART Data, Associate with AP & Send Request Message Containing the UART Data
  factory R & reboot
  Associate module to AP
  set ip proto 18 // set HTTP client mode
  set ip host 0 // IP address of web server
  set dns name www.rovingnetworks.com // OR DNS name
  set ip remote 80 // Web server port
  set comm remote GET$/server3.php?value= // Set request message header
  set uart mode 2 // Automatically connect using trigger mode
  set sys trigger 1 // Wake up on uart RX data
  set sys sleep 10 // Put WiFly module to sleep after 10 seconds
  set option format 1 // Sends out HTTP header
  set comm timer 2500 // Allows multiple keystrokes per request
  save & reboot
In Tera Term, Type Characters to Wake Module, Associate to AP & Send Data as HTTP Message to Web Server
  NOTE: You Cannot Send both Sensor & UART Data in Same Request Message

## Slide 63: Lab 4: Auto-Posting Serial Data
OPEN*SEND-WEBPOST HTTP/1.1 200 OK Date: Mon, 06 Dec 2010 18:25:36 GMT Server: Apache X-Powered-By: PHP/5.2.13 Connection: close Content-Type: text/html
Server accepted values <br />
ID: 0<br /> VALUE: oving Data with first byte missing RTC: 0 *CLOS*
When Serial UART Data Arrives, Module Auto-Connects to Web Server & Sends
  GET /server3.php?value=<user’s serial data> \n\n
NOTE: First Data Byte Dropped because Module Must Initialize before Sending Data over Wireless Interface
To Avoid This Issue, Module Should Wake on CTS Signal Using set sys trigger 2 or Send First Byte Twice

## Slide 64: Lab 4: Conclusion
Module Supports HTTP Client Mode Natively
When Configured, Module Can Append
  GPIO values
  Sensor data
  Real-time clock
  Device name
  UART data
Module Can Wake Up on UART Data
  May result in dropping first byte
  Waking up on CTS is better option

## Slide 65: Lab 5: Access Point Mode
Advantages
  Enables Android devices to talk to modules without infrastructure
  Runs DHCP server
  Supports up to 10 clients
  Supports routing between clients
  Supports WPA2-AES personal security

## Slide 66: Lab 5: Creating a Default AP Network
Download Firmware Supporting AP Mode via FTP
  RN-131: ftp update wifly-241.img
  RN-171: ftp update wifly7-241.img
  RN-370: ftp update wiflyA-241.img
Install Jumper at J6 to Enable AP Mode in Hardware
  SSID: WiFlyAP-XX, where XX is last two bytes of MAC address
  Channel: 1
  DHCP server: Enabled
  IP address: 1.2.3.4
  Netmask: 255.25.5255.0
  Gateway: 1.2.3.4

## Slide 67: Lab 5: Create Custom AP Network in Software
Create Custom AP Network with User-Defined Settings
  set wlan join 7 // Create AP mode network
  set wlan channel <value> // Specify channel to create // network
  set wlan ssid <string> // Set up network SSID
  set ip dhcp 4 // Enable DHCP server
  set ip address <address> // Specify IP address
  set ip net <address> // Specify subnetmask
  set ip gateway <address> // Spcify gateway
  save // Store settings
  reboot // Reboot module in AP mode

## Slide 68: Lab 5: Connect to AP Network Created by Module
From PC/Mobile Phone/Tablet, Connect to Module-Created Network
Module Displays Client’s Device Name

## Slide 69: Lab 5: View Associated Devices & Lease Times
View Device Lease Times
  show lease
View List of Connected Devices
  show associated

## Slide 70: Wi-Fi Training Session
Questions